## Slide 1: Motion Corrected CS MRI
Haris Jeelani

## Slide 2: Introduction
Magnetic Resonance Imaging scans are a non-invasive and painless procedures.
Unlike X-rays and CT scan MRI does not use ionizing radiation (which is potentially harmful to the patient).
Uses powerful magnetic fields to encode the frequency and phase of the water molecules in body.
Popular for Brain Imaging. We work on Cardiac MRI: improve resolution and remove motion.

## Slide 3: More than 10 years ago …
Uniform Sampling.
Recon is very fast.
Major Drawback: Acquisition is very slow.
Frequency Encoding
Phase Encoding
Ref: H. Jung (k-tFOCUSS data)
Abs value
ifft2
(After repeating for all frames)

## Slide 4: Undersampling
Try to acquire less data by skipping lines to speed up the acquisition.
Aliasing:

## Slide 5: Compressed Sensing
(clockwise from top right) Emmanuel Candès, Justin Romberg, David Donoho and Terence Rao.
No need to use Nyquist sampling if the signal is sparse in the representation basis that is incoherent with the sensing basis.[Picture in next slide].
Random Sampling (non uniform works too) helps satisfy the Restricted Isometry Property [will not be discussed] of CS.
MRI signal can be sparse in different domains, Eg: Total Variation.
So, fix Total Variation as your representation basis and sense randomly in k-Space (Fourier) to make compressed sensing work for MRI.

## Slide 6: Matrix Representation of CS-MRI
∫
Matrix that spirally selects the samples
Fourier Domain
(Sensing Basis)
Temporal TV Total Variation Domain
(Representation Basis)
Measurements from the scanner
Signal that we have to recover. (Take Inverse TV to see the actual image).
Thanks to Dr. Yang and Dr. Salerno for the data.

## Slide 7: Motion in MRI
We use temporal TV because there is redundancy along the temporal direction in cardiac MRI. Thus can lead to sparsity.
When the object moves over time the redundancy decreases.
This causes a blur in the image, especially near the boundaries and heart wall.
– frame as a function of pixel values –

## Slide 8: Phase Shift Property (very cool)
[X Y] = [59 167]
Index = 252
[X Y] = [99 167]
Index = 252
FT Domain

## Slide 9: Motion Correction
Choose a Reference Image in k-space ().
Minimize the difference between phase shifted moving images () and to improve temporal consistency.
for t = 1: no of frames.
where
end
Use ‘r’s to correct k-space data and perform Compressed Sensing Reconstruction on motion corrected data.

## Slide 10: Improve Accuracy using center of k-Space.
Get rid of high frequency noise that is found on the periphery of k-Space by cropping the center of k-Space.
We can still preserve most of the information even after doing that.
Use center of k-Space to estimate the phase shifts but apply these phase shifts to whole k-Space after estimation.
Results >>

## Slide 11
H
F
R
L
H
F
R
L
Time
With Motion
After k-Space motion estimation & compensation
After k-Space motion estimation & compensation
With Motion (1 frame)
Dr. Michael Salerno (BME)
Dr. Yang Yang (BME)
Dr. D. S. Weller (ECE)
Haris Jeelani (EE)

## Slide 12
THANK YOU